## Slide 1: AI-Based Sinhala Voice-Controlled Home Automation with Noise Reduction
Final Year Individual Project Defence
Kasundi Perera
June 2026
github.com/kasundisandalika-netizen

## Slide 2: The Problem
Voice automation systems fail in typical homes due to:
  1. Environmental Noise
    Stationary (fans, AC) and Non-Stationary (street traffic, babble)
  2. Low-Resource Language
    Sinhala lacks large ASR datasets, leading to poor baseline accuracy
  3. Security Gap
    Lack of biometric verification in standard smart speakers

## Slide 3: The Solution
End-to-End Edge Deployed System Architecture:
  Mic -> Wake Word -> VGDWF Filter -> ASR -> Biometrics -> ESP32 Control
Key Metrics:
  Online ASR Accuracy: 88.8%
  Offline ASR Accuracy: 83.5%
  Edge Latency: ~120ms (Raspberry Pi 4)

## Slide 4: Research Objectives
1. Evaluate 5 established DSP noise reduction baselines.
2. Design a novel VAD-Guided Dynamic Wiener Filter (VGDWF).
3. Compare Offline (Vosk) vs Online (Google Cloud) ASR engines.
4. Deploy securely on a Raspberry Pi 4 edge device with ECAPA-TDNN.

## Slide 5: Research Gap Analysis
Comparison with Alexa / Google Home / Academic works:
  Sinhala Support: Only This Project
  Offline Edge Deployment: This Project (RPi 4)
  Speaker Verification: This Project (ECAPA-TDNN)
  Custom Noise Filter: This Project (VGDWF)
  Privacy Preserving: This Project (100% Local)

## Slide 6: Proposed Custom Method: VGDWF
VAD-Guided Dynamic Wiener Filter:
  Step 1: Dual-Feature VAD
    Uses Log-Energy and Normalized Spectral Entropy
  Step 2: Dynamic Noise PSD Estimation
    Updates only during noise frames via exponential average
  Step 3: Adaptive Oversubtraction
    Scales between 1.0 and 3.0 based on local SNR

## Slide 7: Testing Framework (24 Scenarios)
4 Noise Types:
  White Noise, Fan/AC, Street Traffic, Cafe Babble
3 SNR Levels:
  -5 dB, 0 dB, 10 dB
2 ASR Engines:
  Google Cloud STT (Online), Vosk (Offline)

## Slide 8: Results: Online ASR (Google STT)
Average Command Accuracy:
  Unfiltered: 57.5%
  Butterworth: 66.1%
  Spectral Subtraction: 75.4%
  Static Wiener: 77.3%
  Wavelet Denoising: 78.8%
  Spectral Gating: 80.3%
  Proposed VGDWF: 88.8%

## Slide 9: Results: Offline Edge (Vosk)
Average Command Accuracy:
  Unfiltered: 52.5%
  Spectral Gating: 75.9%
  Proposed VGDWF: 83.5%
Offline Edge Viability:
  Only 5% drop vs Cloud STT
  8x lower latency (120ms vs 1000ms)

## Slide 10: Conclusions
1. Superior Performance
  VGDWF outperforms all baselines in every scenario.
2. Optimal Edge Architecture
  Vosk + VGDWF yields 83.5% offline accuracy.
3. Robust Security
  ECAPA-TDNN prevents unauthorized smart home control.